## Slide 1: NPC

## Slide 2
NPC Architecture
Layered Architecture View

## Slide 3: NPC Deployment Architecture
Mode of deployment – SM and ME

## Slide 4
NPC geo-redundancy
ME
OSS
NPC Site #1
NPC Site #2
Geo-replication
ME
Region 1
SM1
SM2
SM sites are Active-Standby (hot)
Service definition: SM has master copy & distributes to sites
SM selects device home or is instructed by OSS
SM maintains the device home location & each ME does geo-replication
Geo-replication
ME
NPC Site #3
NPC Site #4
ME
Region 2
Geo-replication
ME
NPC Site #5
NPC Site #6
ME
Region 3
Geo-replication
ME sites are Active-Active – No idle hardware
REST SOAP
1+1 mated pair
Multi-node support increases deployment flexibility for large operators by dividing into regions and supporting a combination of Policy and Charging nodes
Notes: reliability

## Slide 5: NPC SM & ME systems configured with all modules
Apps
ComSvcs
NPC SM System
Provisioning, API requests
OAME
API
IOH
Core
IOH
NPC ME System
DB
OAME
* Aux VMs host Service Discovery and Configuration (SDC) and always use exactly 5 VMs
5G, Diameter peers
Provisioning,
API requests,
SPR traffic
Notifications,
IT system interaction
DB replication
CDR
AUX*
SM App
IOH
DB
API to SPSs, IPv6 to ME
AUX*
Legend for VM engineering:
1 + 1
N + K
2*(N + K)
SU VM groups shown as gold, blue, and green boxes
DB replication
Operation and Management, logging
Operation and Management, logging
Provisioning, API requests, SPR traffic

## Slide 6: NPC VNF lifecycle management
Via Nokia CBAM VNFM
Create
Modify
Instantiate
Heal, auto-Heal
Backup, restore
Disaster recovery
Terminate
Delete
Scale out/in, auto-scale
Upgrade
  Life Cycle Events
  Instantiate VNF
  Healing
  Scale out /Scale –In
  Terminate VNF
  Delete VNF
  Backup and Restore
  VNF Network Upgrade
  VNF Disaster recovery
  Auto Healing
  Auto Scaling

## Slide 7
Agenda
Product overview & main benefits
Product functionalities
Interfaces & integration capabilities
Policy Rules
Main use cases
Q&A session

## Slide 8: Policy Management
NPC can provide the following to gateways
  QoS, including rates (down/up) and priority
  PCC rules to define gateway behavior for a session/flow
  Redirects
  Charging related policies (such which rating group to use)
NPC can accept or reject/terminate sessions
It can register for events from the gateways
  Be notified when events occur, such as a RAT Type change
  Usage monitoring, such as reporting when a UE has used 20MB of data
Policies are provided on request and can be pushed for updates
Sample policy behaviors

## Slide 9: Policy Management
NPC provides the Policy and Charging Rules Function (PCRF) in 4G/LTE
  It provides policy to gateways (PCEFs)
NPC provides the Policy Control Function (PCF) in 5G
  Both can be provided in the same NPC instance – a combined PCRF+PCF
NPC can provide policy based on a wide variety of inputs, including
  Subscription type
  Type of device
  Location (such as MCC/MNC, GGSN IP address, cell tower)
  Configured subscriber/device data
  Time of day / day of week
  Usage related policies, such as CHF/OCS counter values
Policy control

## Slide 10: Policy Management
Networks need policy management
RNC
Gx
Sd
Sy
OCS
REST
Ud LDAP
Rx
NPC
AF/IMS
NPC can use NCC or a third-party OCS.
IMS
SGSN/SGw
GGSN/PGw
DPI
MME
OSS/BSS
SPR
Charging
PCRF
GERAN
CDN/ Video Opt.
Provides policy to network elements to enable subscriber experience

## Slide 11: NPC
NPC will provide policy for both 4G/LTE (a PCRF) and 5G (a PCF)
Provides a single consistent view of a subscriber / device
Manage policies across both 4G and 5G
  Use common rules/information where appropriate, or 4G/5G specific rules when needed
Migrate subscribers more easily from the 4G network to the 5G network
Ease the migration to 5G
AF
PCF
CHF
SMF
AMF
PCRF
Gx
Rx
OCS
AF/IMS
Sy
RAN
UPF
SGSN/SGw
GGSN/PGw
4G
5G
N5
N28
N7
N15

## Slide 12
Agenda
Product overview & main benefits
NPC Architecture
Interfaces & integration capabilities
Policy Rules
Main use cases
Q&A session

## Slide 13: Policy Management
Rules-based flexibility
  Each mapping can have multiple keys and outputs
  Used enter long list such as MCC/MNC location, cell tower lists, plans/OCS counter states, QoS related attributes, etc.
  Scripting editor rather than clicking forms
  Cut & paste rule code
  Autocomplete and syntax checking
  Decouple independent rule logic that can be called as variable in main Business Rules
  Can use Mappings for further simplification
New rules editor
Variables
Mappings
The core of the rules engine is carried forward from the DSC

## Slide 14
Policy rules: Why use a rules engine and what does it do?
OCS=Online charging system CHF=5G Charging function
Nokia Policy Controller
OCS/CHF
Network
Subscriber DB
Gateway/TDF
Other influencing events
Provides highly flexible and efficient policy definition
Rules are evaluated when an event occurs
Rules are only used when a custom policy is needed
When defining policy, or authoring rules, many inputs can be used to determine the policy
An easy and controlled way to move rules from the lab to production

## Slide 15: NPC Rules
Rules are edited in the GUI using a simple IF (condition) THEN (action) format
They are entered as text with autocompletion and syntax checking
Writing rules

## Slide 16
Agenda
Product overview & main benefits
Product functionalities
Interfaces & integration capabilities
Policy Rules
Main use cases
Q&A session

## Slide 17: Policy Management
To each their own…
Location based
(roaming, in region, home)
Device type based policy (type/model)
Use lookup tables (custom data)
RAT based policies
Time of day, day of week policies
Notifications (email, SMS, web service)

## Slide 18: Sample use cases
A variety of location information is available to determine policy
MCC / MNC indicates which network a device is on
  Can be used for roaming scenarios
Cell tower Ids can be used for fine-tuned location information
  Such as policy at a subscriber's home location
  Or in/around metro/subway stations
The gateway IP address can be used
  Sometimes used if MCC / MNC are not sufficient
Location based

## Slide 19: Sample use cases
Similar to the examples shown, rules can be tailored in many ways, including
  Policy based on the DNN/APN – different privileges for different DNNs/APNs
  Policy based on the slice (5G)
  User equipment type based policy
  Access type dependent policy (such as by RAT-Type)
Policy may push PCC rules to the gateway
  Can enable redirects of flow-based handling of traffic
The policy rules can send notifications to the subscriber
  By email, SMS or web service call
OSS/BSS facing APIs allow for self-care
  Subscribers can be provided a portal to configure policies
Many possibilities…

## Slide 41
Introduction to Deployment
Distributed SM
Distributed ME
Integrated SM+ME

## Slide 42
Images download source
VNF Images
https://repo.lab.pl.alcatel-lucent.com/sps-generic-candidates/spsmainbuild/SPS_22_0_I24/
Maestro Images
https://repo3.cci.nokia.net/sps-generic-candidates/DevOps_images/

## Slide 43
Planning the allocation of external IP addresses to the VNF VMs
Internal IP
The IPs allocate to internal network
External IP
The IPs allocate to external network
Subnet
Internal 192.168.3.10/24
External 10.68.125.70/24

## Slide 44
Agenda
Product overview
Introduction to Deployment
Deploying maestro VM
VNF generator tool
SM /ME Deployment

## Slide 45
Deploying maestro VM
Download maestro VM image and hot yaml file to UC node
Configure heat yaml file.
Deploy maestro VM as a heat stack

## Slide 46
Starting VNF generator tool on maestro VM
Download VNF generator tool to maestro VM
Download csar package to maestro VM
Create and prepare vnf generator workspace
Starting vnf editor inside sps instantiation docker
Using vnc client to reach vnf generator graphical too

## Slide 47
Deployment
  Installation Guide/Release Notes to be downloaded from NOLS - Link
  Sample JSON file
Health Check-up
  Check the status of services

## Slide 48
Documentation Navigation
Training Session
  Link
Policy User Guide
  Link
VNF Installation and Upgrade Guide
  Link
VNF Operation Administration and Maintenance Guide
  Link
VNF Overview
  Link

## Slide 49
System Health & Health Checks
Nokia Policy Controller
The system health is a resultant value derived from the health of constituent components.
The system must be monitored for degradation of health (systems not working at rated performance, or not working at all) and troubleshooting activities should be performed as needed.
Health monitoring is composed of several checks that are run on several component systems. Few to list are as below
  Disk usage
  HA to ensure active-standby operation
  Reduced availability for N+K local redundancy. Loss of more than K systems results in an outage
  All services monitoring running on NPC SM and ME VMs.
To check sps basic health of VMs and its services ‘sps-status’ command can be used and executed using tpaadmin user on the OAME node (preferred).
Monitor status of different services like aerospike, LTM, kafka, traffic to nodes on IOHD etc which are down and performing actions to restore them.

## Slide 50
System Health & Health Checks (contd..)
Nokia Policy Controller
Several services are monitored by NPC. Key services are listed under -
  Aerospike Cluster Service, XDR Service
  CDR Service
  Charging application Service
  CKEY Service
  CMDB Service
  DiameterIO Service
  ETCD Cluster Service
  httpIO Service, SMAPP Service
  KAFKA Service, TEM Service, TRSCHEDULER Service
  Loadbalancer Service, LTM Service, Notification Service, Policy app Service, Provisioning Service, Rollback Service

## Slide 51
Agenda
System Health & Health Checks
NPC Alarms
NPC Measurement Collection
Measurements in Prometheus & Grafana
Sample Screenshots
Q&A

## Slide 52
NPC Alarms
Nokia Policy Controller
Alarms are generated to alert operators of abnormal behavior. Alarms are raised by the Policy, Charging, and Service Manager (SM) applications as well as by the system and Operation Administration Maintenance Endpoint (OAME).
These alarms are meant to be sent to the Environmental Management System (EMS) that displays them.
The alarming service is provided across a cluster of machines in a cloud environment and supports the following:
  southbound interface that allows applications to generate alarms
  alarm management that includes alarm processing, storage and lifecycle management
  northbound interface (SNMP v2c/v3) that reports alarms to the EMS.
Active alarms are stored in the ETCD backend. To see active alarms, run the following command on the Active OAME VM:
curl http://localhost:8182/api/alma/alarms

## Slide 53
Agenda
System Health & Health Checks
NPC Alarms
NPC Measurement Collection
Measurements in Prometheus & Grafana
Sample Screenshots
Q&A

## Slide 54
NPC Measurement Collection
Nokia Policy Controller
NPC collects a broad range of measurements to provide a rich set of data for understanding the load and behavior of the system and its network integration.
The metrics are available to examine on the NPC itself and can also be retrieved by external systems for offboard analysis.
Metrics are gathered onto the central OAME nodes in each NPC, where the Prometheus server and database are located.
Both OAME nodes run the Prometheus server and both actively collect measurement data from the clients and store the data in their own local databases, such that all measurements data continues to be available following an OAME switchover.
A Prometheus client runs on all the nodes that are recording metrics to be collected by the Prometheus server on the OAME.
Measurement collection config GEN3GPPXML file format as shown in figure to the right.

## Slide 55
NPC Measurement Collection (contd..)
Nokia Policy Controller
NPC has two modes of measurement collection: CSV and PROMETHEUS
When the measurement mode is CSV then NPC generates the metrics data in CSV format on the OAME nodes under /appdata directory. These files can be further pulled by respective integrating monitoring agent NE.
When the measurement mode is PROMETHEUS then NPC generates the metrics data in XML format on the OAME nodes under /appdata/meas directory. These files can be further pulled by respective integrating monitoring agent NE.
The tool for configuring metrics mode is located under /opt/tpa/bin directory. After execution, for a change to take place, we need to restart the application on all the VM nodes.
configure-metrics-mode -m <METRICS_MODE>
Where <METRICS_MODE> can be either ‘csv’ or ‘Prometheus’.

## Slide 56
Agenda
System Health & Health Checks
NPC Alarms
NPC Measurement Collection
Measurements in Prometheus & Grafana
Sample Screenshots
Q&A

## Slide 57
Measurements in Prometheus & Grafana
Nokia Policy Controller
Prometheus provides a multi-dimensional data model with time series
data identified by metric name and key/value pairs.
It is a free software application used for event monitoring and alerting.
A flexible query language is supported for retrieving data from the
database. It uses an HTTP pull model with real time alerting. It is licensed
under Apache 2 License
Prometheus GUI queries should be executed on OAME standby node.
Prometheus GUI can be accessed at:
http://<OAM IP>:9090
A sample snap of the Prometheus GUI is shown in the figure to the right

## Slide 58
Measurements in Prometheus & Grafana (contd..)
Nokia Policy Controller
Grafana is a multi platform open source analytics and interactive visualization web application which provides charts, graphs and alerts for the web when connected to supported data sources.
Grafana keys are configured in vnf extensions json file during the time of deployment. In a standard deployment the default values are used as it is.
The Grafana admin user must create users on the dashboard to access specific graphs/metrics.
Each instance of Grafana software works independently on each OAME and must be configured on both OAME nodes i.e. active and standby.
Grafana GUI can be accessed at:
https://<OAM IP>:8003
Default first time admin login credentials ‘admin/admin’ can be used.
Sample dashboard view is as shown in the snapshot to the right.

## Slide 59
Agenda
System Health & Health Checks
NPC Alarms
NPC Measurement Collection
Measurements in Prometheus & Grafana
Sample Screenshots
Q&A

## Slide 60
Sample Screenshots
Nokia Policy Controller

## Slide 61
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 62
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 63
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 64
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 65
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 66
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 67
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 68
Sample Screenshots (contd..)
Nokia Policy Controller

## Slide 69
NPC Deployment Pre-Requisites :
1. CIQ – containing the IP information/allocation subnets, flavour, vCPU, vRAM, vDISK, cinder information, custom system preference
2. Site LLD
3. CBIS/OpenStack GUI Access with Project User.
4. CBAM admin access to create spsclient user and extract secret key
Nokia CA Certificate of CBIS/OpenStack should be available locally.
Network creation
7. Flavor Creation as per NPC Dimensioning which will be configured in JSON file & required for allocating the resources.
8. Verification of the resources allotted to CBIS/OpenStack Project User for NPC deployment for Number of VM Instances, vRAM, vCPU, vDISK & Storage Volume .
9. Computes availability across different zones (Confirmation from cloud team that sufficient computes are available in Cloud Environment for NPC installation)

## Slide 70
Cloud Terminology Overview
1. CIQ – containing the IP information/allocation subnets, flavour, vCPU, vRAM, vDISK, cinder information, custom system preference
2. Site LLD
3. CBIS/OpenStack GUI Access with Project User.
4. CBAM admin access to create spsclient user and extract secret key5. Nokia CA Certificate of CBIS/OpenStack should be available locally.
6. Flavor Creation as per NPC Dimensioning which will be configured in JSON file & required for allocating the resources.
7. Verification of the resources allotted to CBIS/OpenStack Project User for NPC deployment for Number of VM Instances, vRAM, vCPU, vDISK & Storage Volume (for Cinder Volume).
8. Computes availability across different zones (Confirmation from cloud team that sufficient computes are available in Cloud Environment for NPC installation)

## Slide 71
NPC Deployment Preparation:
1. Cloud Setup Readiness for NPC Instantiation
2. Download Images
3. Upload Images
4. Network Creation
5. Flavor Creation
6. JSON File Preparation

## Slide 72
NPC Deployment Preparation cont..
Cloud Setup Readiness for NPC Instantiation:
Nokia CA Certificate
Make sure that External & Internal Networks are already allocated to project & sufficient IP are available for NPC Installation along with CBAM.
Images should be downloaded & uploaded in Glance before starting respective Instantiation. ​

## Slide 73
NPC Deployment Preparation cont..
NPC Images and CSAR packages download :
Images can be downloaded from below URLs:
https://download-emea.support.nokia.com/cgi-bin/Download.pl
VNF generator:
CSAR Packages:
https://download-emea.support.nokia.com/cgi-bin/Download.pl
VNF Generator:
CSAR Package:

## Slide 74
Images download source
VNF Images
https://customer.nokia.com/support/s/
Maestro Images
https://repo3.cci.nokia.net/sps-generic-candidates/DevOps_images/

## Slide 75
NPC Deployment Preparation cont..
Images required for NPC and Maestro:
CSAR Package:
Images Name
AUXILIARY QCOW2
CDR QCOW2
DATABASE QCOW2
SM_APP QCOW2
COMMON_SERVICES QCOW2
DIAMETER_IOH QCOW2
POLICY_CHARGING_APP QCOW2
OAME QCOW2
LOADBALANCER_ME QCOW2
LOADBALANCER_SMIG QCOW2
Maestro-HOT-2102.0.0-R1-73.yaml
Maestro-2102.0.0-R1-73.qcow2

## Slide 76
NPC Deployment Preparation cont..
Network creation:
Use below mentioned command from undercloud hypervisor in order to perform network and Subnet creation
Command:
Network creation
neutron net-create G-5GSAKANSHI-VL1057-NPCData-ExtOAM --provider:network_type vlan --provider:physical_network physnet0 --provider:segmentation_id 1057
Subnet creation
neutron subnet-create --name G-5GSAKANSHI-VL1057-NPCData-ExtOAM_Subnet --gateway 10.16.26.206 G-5GSAKANSHI-VL1057-NPCData-ExtOAM 10.16.26.192/28
Use these two commands for all the networks mentioned in the IP sheet.

## Slide 77
NPC Deployment Preparation cont..
Images Upload on CBIS:
Transfer these images one by one to undercloud hypervisor and then run glance command corresponding to image transferred.
Command:
#glance image-create --name <NPC version>.<image name or id> \--disk-format qcow2 \ --file <NPC version>.<image name or id>.qcow2 \ --container-format bare --property hw_vif_multiqueue_enabled=true
Command example:
#glance image-create --name SPS_21_8_I118.AUXILIARY --disk-format qcow2 --container-format bare --file SPS_21_8_R1_SPS_21_8_I118.AUXILIARY.qcow2 --property hw:vif_multiqueue_enabled=true

## Slide 78
NPC Deployment Preparation cont..
Flavour Creation:
Use below mentioned commands from undercloud hypervisor in order to create flavour as per requirement mentioned in the LLD.
Example:
nova flavor-create c8_r12_d100 auto 12288 100 8
nova flavor-create c12_r12_d100 auto 12288 100 12
Change the cpu, ram and disk as per mentioned in LLD.

## Slide 79
NPC Deployment Preparation cont..
JSON File Preparation
To prepare json file take details from the LLD and Ip sheet
1. From the downloaded images, untar the “OpenStack CSAR Package”.
2. Edit the JSON File Templates “SPS_21_8_I118_SM_VNF_CONF.json” and “SPS_21_8_I118_SM_SDC_CONFIG.json” for SM configuration.
3. Edit the JSON File Templates “SPS_21_8_I118_ME_VNF_CONF.json” and “SPS_21_8_I118_ME_SDC_CONFIG.json” for ME configuration.
4. Do not modify the default_conf.json files.
5. Enter the other parameter values wherever “<MUST FILL>” is mentioned in JSON files, which will include Internal/External Network Name, IP address, VIP address, cinder volume,etc.
6. Similarly fill the SDC Config file parameters.

## Slide 80
Deploying maestro VM
Download maestro VM image and hot yaml file to UC node
https://repo.lab.pl.alcatel-lucent.com/policy-generic-candidates/DevOps_images/
Configure heat yaml file.
Deploy maestro VM as a heat stack

## Slide 81
SM /ME Instantiation through Maestro

## Slide 82
Prerequisite files for Instantiation through Maestro
ca.crt.pem
cbam2key.pem
openrc.sh file
cloud-config.yaml
5. SM & ME VNF and SDC files

## Slide 83
SM Instantiation through Maestro
Execute SM instantiation command on Maestro:
Example:
/usr/local/bin/maestro ace sps-instantiate -d /opt/sps/SPS_21_2_I106 -i /opt/sps/configs/SPS_21_2_I106_SM_SDC_CONFIG.json -j /opt/sps/configs/SPS_21_2_I106_SM_VNF_CONF.json -s sm SPS_21_2_R1_SPS_21_2_I106

## Slide 84
ME Instantiation through Maestro
Execute ME instantiation command on Maestro:
Example:
/usr/local/bin/maestro ace sps-instantiate -d /opt/sps/SPS_21_2_I106 -i /opt/sps/configs/SPS_21_2_I106_ME_SDC_CONFIG.json -j /opt/sps/configs/SPS_21_2_I106_ME_VNF_CONF.json -s me SPS_21_2_R1_SPS_21_2_I106

## Slide 85
NPC deployment through CBAM

## Slide 86
Deployment steps:
1. CBAM package creation through VNF generator for SM & ME
2. Upload CBAM packages on CBAM GUI to create Catalog
3. SM instantiation through CBAM
4. ME instantiation through CBAM
5. Validate stack on CBIS post Instantiation

## Slide 87
Starting VNF generator tool on maestro VM
Download VNF generator tool to maestro VM
Download csar package to maestro VM
Create and prepare vnf generator workspace

## Slide 88
CBAM package creation
CBAM Package creation on Maestro:
 Make sure appropriate vnf generator packages are saved on Maestro
 SM and ME VNF & SDC config files are placed on desired path /opt/sps/configs in Maestro

## Slide 89
CBAM package creation
Commands to create CBAM package
 For SM
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Example: # ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_SM_VNF_CONF.json -b -o /tmp/SM
For ME:
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Where SM & ME packages will be generated in /tmp
Example: ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_ME_VNF_CONF.json -b -o /tmp/ME

## Slide 90
Catalog creation on CBAM for SM and ME:

## Slide 91
Catalog creation on CBAM:
In the CBAM GUI, click the options button with three horizontal lines and then select Catalog. The Catalog pane appears.
Commands to create CBAM package
 For SM
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Example: # ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_SM_VNF_CONF.json -b -o /tmp/SM
For ME:
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Where SM & ME packages will be generated in /tmp
Example: ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_ME_VNF_CONF.json -b -o /tmp/ME

## Slide 92
Catalog creation on CBAM:
Upload VNF package for SM:
Commands to create CBAM package
 For SM
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Example: # ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_SM_VNF_CONF.json -b -o /tmp/SM
For ME:
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Where SM & ME packages will be generated in /tmp
Example: ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_ME_VNF_CONF.json -b -o /tmp/ME

## Slide 93
Catalog creation on CBAM:
Commands to create CBAM package
 For SM
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Example: # ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_SM_VNF_CONF.json -b -o /tmp/SM
For ME:
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Where SM & ME packages will be generated in /tmp
Example: ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_ME_VNF_CONF.json -b -o /tmp/ME

## Slide 94
Catalog creation on CBAM:
Commands to create CBAM package
 For SM
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Example: # ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_SM_VNF_CONF.json -b -o /tmp/SM
For ME:
./vnf_gen.py -i <path of SM_VNF_JSON file> -b -o /tmp/SM
Where SM & ME packages will be generated in /tmp
Example: ./vnf_gen.py -I /opt/sps/configs/SPS_21_5_I73_ME_VNF_CONF.json -b -o /tmp/ME

## Slide 95
NPC SM & ME Instantiation Steps:
After Catalog creation for SM & ME, Follow below procedure for SM & ME
In the CBAM GUI, do the following:
i. Create SM/ME VNF with a particular CSAR package using the procedure Creating VNF
ii. Modify this SM/ME VNF with the VNF Extension file generated for this VNF using the procedure Modifying VNF.
iii. Instantiate SM/ME VNF with the Scalable file generated for this VNF using the procedure Instantiating VNF.

## Slide 96
Create VNF for SM

## Slide 97
Create VNF for SM

## Slide 98
Create VNF for SM

## Slide 99
Modify VNF for SM

## Slide 100
Modify VNF for SM

## Slide 101
Modify VNF for SM

## Slide 102
Modify VNF for SM

## Slide 103
Modify VNF for SM

## Slide 104
Modify VNF for SM

## Slide 105
Modify VNF for SM

## Slide 106
Modify VNF for SM

## Slide 107
INSTANTIATE SM VNF

## Slide 108
Instantiate SM VNF

## Slide 109
Instantiate SM VNF

## Slide 110
Instantiate SM VNF

## Slide 111
Instantiate SM VNF

## Slide 112
Instantiate SM VNF

## Slide 113
Instantiate SM VNF

## Slide 114
Instantiate SM VNF

## Slide 115
Instantiate SM VNF

## Slide 116
Instantiate SM VNF

## Slide 117
Instantiate SM VNF

## Slide 118
INSTANTIATE ME VNF
1. Create VNF for ME
2. Modify ME VNF
3. Instantiate ME VNF

## Slide 119
Create VNF for ME

## Slide 120
Create VNF for ME

## Slide 121
Modify ME VNF

## Slide 122
Modify ME VNF

## Slide 123
Modify ME VNF

## Slide 124
Modify ME VNF

## Slide 125
Modify ME VNF

## Slide 126
Modify ME VNF

## Slide 127
Modify ME VNF

## Slide 128
INSTANTIATE ME VNF

## Slide 129
Instantiate ME VNF

## Slide 130
Instantiate ME VNF

## Slide 131
Instantiate ME VNF

## Slide 132
Instantiate ME VNF

## Slide 133
Instantiate ME VNF

## Slide 134
Instantiate ME VNF

## Slide 135
Instantiate ME VNF

## Slide 136
Instantiate ME VNF

## Slide 137
Validate Stack creation on CBIS GUI

## Slide 138
Validate Stack on CBIS GUI

## Slide 139
VNF status on CBAM

## Slide 140
Deployment
  Installation Guide/Release Notes to be downloaded from NOLS - Link
  Sample JSON file
Health Check-up
  Check the status of services

## Slide 141
Documentation Navigation
Training Session
  Link
Policy User Guide
  Link
VNF Installation and Upgrade Guide
  Link
VNF Operation Administration and Maintenance Guide
  Link
VNF Overview
  Link

## Slide 142
NPC
Access Network Charging Identifier
Ivo Tanouchev
03-06-2022

## Slide 143: Agenda
Feature overview
Access Network Charging Identifier operation
SM view

## Slide 144: Feature overview
Tittle: NPCART-134 Access Network Charging Identifier Support
The EPIC asks to support propagation of N7 session Access Network Charging Identifier to AF when such is requested
The exchange with IMS applies to both Gx and N7 as well as Rx and N5. NPC Release 22.5 does not support N5 interface, and the focus of this feature is Rx to N7
NPCART-134 scope
Confidential. Not for distribution or disclosure outside NOKIA

## Slide 145: Feature overview
Sravan Sajeev, design
Nadia Spido, QA
Ivo Tanouchev, PO
NPCART-134 team
Confidential. Not for distribution or disclosure outside NOKIA

## Slide 146: Feature overview
The AF may request to the PCF the Access Network Charging Identifier by subscribing to the CHARGING_CORRELATION_EXCHANGE (1) within the Specific-Action AVP
  The PCF shall provide the Access Network Charging Identifier in the Rx:AA Answer if already known
  If not known, PCF shall request the identifier to the SMF by including the "PolicyCtrlReqTriggers" attribute with the value "AN_CH_COR“ , if not already installed; and the "lastReqRuleData" attribute
  When the PCF gets the identifier from SMF, it shall send Rx:RAR to the AF with the obtained identifier
There could be different Access Network Charging Identifier per service flow i.e., dynamic PCC rule
TS 29.212 Rel. 12.9, from 24-07-2015 added support/indication for IP-CAN-Session-Charging-Scope
  Automatically available in TS 29.512 for 5G N7 SBI
  NPC did not support this for 4G Diameter, and no specific work was done either, but added support for the AVP
3GPP Procedure
Confidential. Not for distribution or disclosure outside NOKIA
The 5G way of doing it
Day one of TS 29.214, Rel 7 even
TS 29.212 only talks about it in Rel 8, Version 8: CHARGING_CORRELATION_EXCHANGE (28)

## Slide 147: Agenda
Feature overview
Access Network Charging Identifier operation
SM view

## Slide 148: Access Network Charging Identifier operation
One liner, or two
Confidential. Not for distribution or disclosure outside NOKIA
Access Network Charging Identifier operation is handled by NPC code. There is no Rules logic involved
Unlike similar functionalities, there is no Feature number involved

## Slide 149: Access Network Charging Identifier – session level Acc Net Charg Id
Rx: AAR Specific-Action=CHARGING_CORRELATION_EXCHANGE (1)
Rx: AAA
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=12345678
UE1
AF
Confidential. Not for distribution or disclosure outside NOKIA
NPC
SMF
Npcf_SMPolicyControl_Create
“accNetChId“ {
"accNetChaIdValue":12345678,
"sessionChScope":true }
Npcf_SMPolicyControl_UpdateNotify "pccRules":{ "dynpcc1":{ "pccRuleId":"dynpcc1“}},
"lastReqRuleData":[ {
"refPccRuleIds": [“dynpcc1"], "reqData": [”CH_ID”]
} ],
“policyCtrlReqTriggers” = [”AN_CH_COR”]
Response
If already known
NPC replies with the AN Ch Id regardless of the SA, legacy operation
NPC will not request Triggers
No obvious clause if PCF shall install triggers for the known case
TS 29.512

## Slide 150: Access Network Charging Identifier operation
Access Network Charging Identifier – session level Acc Net Charg Id
Confidential. Not for distribution or disclosure outside NOKIA
SMF provides the Access Network Charging Identifier in the Request and includes Session scope
Access Network Charging Id in Rx:AAA
No trigger installed with the installation of PCC rules

## Slide 151: Access Network Charging Identifier – session level Acc Net Charg Id
Rx: AAR Specific-Action=CHARGING_CORRELATION_EXCHANGE (1)
Rx: AAA
UE1
AF
Rx: RAR Specific-Action= CHARGING_CORRELATION_EXCHANGE (1),
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=12345678
Confidential. Not for distribution or disclosure outside NOKIA
NPC
SMF
Npcf_SMPolicyControl_Create
Npcf_SMPolicyControl_UpdateNotify "pccRules":{ "dynpcc1":{ "pccRuleId":"dynpcc1“}},
"lastReqRuleData":[ {
"refPccRuleIds": [“dynpcc1"], "reqData": [”CH_ID”]
} ],
“policyCtrlReqTriggers” = [”AN_CH_COR”]
Npcf_SMPolicyControl_Update
"repPolicyCtrlReqTriggers":[ “AN_CH_COR" ],
“accNetChIds“:[{
"accNetChaIdValue":12345678,
"sessionChScope":true }]
"ruleReports": [ {
"pccRuleIds":[“dynpcc1"],
"ruleStatus":"ACTIVE“
} ]
Response
If Access Network Charging Id is not known
Not clear we get this
NPC will report this exact AVP structure in the Rx: RAR
TS 29.214

## Slide 152: Access Network Charging Identifier operation
Access Network Charging Identifier – session level Acc Net Charg Id
Confidential. Not for distribution or disclosure outside NOKIA
No Access Network Charging Identifier in the SMF initial Request
No Access Network Charging id
Installing triggers
SMF Update
Rx:RAR

## Slide 153: Access Network Charging Identifier – flow level Acc Net Charg Id
Rx: AAR Specific-Action=CHARGING_CORRELATION_EXCHANGE (1)
UE1
AF
Rx: RAR Specific-Action= CHARGING_CORRELATION_EXCHANGE (1),
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=12345678
Flows:
Media-Component-Number = 1,
Flow-Number =1,
Flow-Number = 2
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=87654321
Flows:
Media-Component-Number = 2,
Flow-Number = 1,
Flow-Number = 2
Confidential. Not for distribution or disclosure outside NOKIA
NPC
SMF
Npcf_SMPolicyControl_Create
Npcf_SMPolicyControl_UpdateNotify "pccRules":{ "dynpcc1":{ "pccRuleId":"dynpcc1"}},
"lastReqRuleData":[ {
"refPccRuleIds": ["dynpcc1", "dynpcc2",…], "reqData": ["CH_ID"]
} ],
"policyCtrlReqTriggers" = ["AN_CH_COR"]
Response
Rx: AAA
Multiple PCC rules possible
Npcf_SMPolicyControl_Update
"repPolicyCtrlReqTriggers":["AN_CH_COR" ],
"accNetChIds" [
{
"accNetChaIdValue":12345678,
"refPccRuleIds”:["dynpcc1", "dynpcc2"]
},
{
"accNetChaIdValue":87654321,
"refPccRuleIds": ["dynpcc3", "dynpcc4"]
}
]
Report can be per PCC rule or most likely per QCI
e.g., two flows: RTP, RTCP

## Slide 154: Access Network Charging Identifier operation
Access Network Charging Identifier – per PCC rule level Acc Net Charg Id
Confidential. Not for distribution or disclosure outside NOKIA
No Access Network Charging Identifier in the SMF initial Request
No Access Network Charging id
SMF Update, Charging Id per PCC rule
Installing triggers
Specify the Charging Id against the Service Flow

## Slide 155: Access Network Charging Identifier – Access Network Charging Address
Rx: AAR Specific-Action=CHARGING_CORRELATION_EXCHANGE (1)
Rx: AAA
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=12345678
UE1
AF
Rx: RAR Specific-Action= CHARGING_CORRELATION_EXCHANGE (1),
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=12345678
Access-Network-Charging-Address = 10.10.10.10
Confidential. Not for distribution or disclosure outside NOKIA
NPC
SMF
Npcf_SMPolicyControl_Create
" accNetChIds " {
"accNetChaIdValue":12345678,
"sessionChScope":true }
"chargEntityAddr": {"anChargIpv4Addr":"10.10.10.10"}
Npcf_SMPolicyControl_UpdateNotify "pccRules":{ "dynpcc1":{ "pccRuleId":"dynpcc1"}},
"lastReqRuleData":[ {
"refPccRuleIds": ["dynpcc1"], "reqData": [”CH_ID”]
} ],
"policyCtrlReqTriggers" = ["AN_CH_COR"]
Npcf_SMPolicyControl_Update
"repPolicyCtrlReqTriggers":[ “AN_CH_COR" ],
" accNetChIds " {
"accNetChaIdValue":12345678,
"sessionChScope":true }
"chargEntityAddr": {"anChargIpv4Addr":"10.10.10.10"}
Response
Outside accNetchIds, single value
Can be received here as well
Not part of initial V15.1.0

## Slide 156: Access Network Charging Identifier – Access Network Charging Address
The 3GPP challenge
Confidential. Not for distribution or disclosure outside NOKIA
TS 29.214
Optional (Single)
Multiple, Optional
TS 29.512
"chargEntityAddr":{
"anChargIpv4Addr":"172.17.104.241",
"anChargIpv6Addr":"1111:111:111:111:111:305:1002:8010",
}
Nested attribute
For NPC chosen to propagate the IPv4 to AF if both present….

## Slide 157: Access Network Charging Identifier operation
Identifier examples
Confidential. Not for distribution or disclosure outside NOKIA
TELUS 4G
BELL
0x6943CFFE
T-Mobile -> no ccNetChId in N7 Request

## Slide 158: Agenda
Feature overview
Access Network Charging Identifier operation
SM view

## Slide 159: SM view
Access Network Charging Identifier support
Confidential. Not for distribution or disclosure outside NOKIA
The support for the Identifier at the PDU session was not completed in 22.5, created NPCART-5688
Currently no Access Network Charging Identifier details are shown in the SM for the PDU session
Re-labeled the “header”, also replaced “AN” with “Access Network” , re-arranged the rows
AF session in SM does not show Access Network Charging Identifier, but has it in Aerospike
4G format really, may change to indicate v4 and v6 addresses
The AN Charging Id if session level
Will be adding Session Scope flag (perhaps redundant)
The Id reported per Service Flow / PCC
Old labels (IPCAN)

## Slide 161: Access Network Charging Identifier – 4G Diameter operation
Rx: AAR Specific-Action=CHARGING_CORRELATION_EXCHANGE (1)
UE1
AF
Rx: RAR Specific-Action= CHARGING_CORRELATION_EXCHANGE (1),
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=123
Flows:
Media-Component-Number = 1,
Flow-Number =1,
Flow-Number = 1
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=456
Flows:
Media-Component-Number = 1,
Flow-Number = 1,
Flow-Number = 2
Confidential. Not for distribution or disclosure outside NOKIA
NPC
PGw
Gx:CCR(I)
Access-Network-Charging-Identifier-Gx:
Access-Network-Charging-Identifier-Value = 123456,
IP-CAN-Session-Charging-Scope = 0,
Access-Network-Charging-Address
Gx:RAR Charging-Rule-Install::=
Charging-Rule-Definition::= dynpcc1, dynpcc2,
Charging-Correlation-Indicator = 0,
ET=CHARGING_CORRELATION_EXCHANGE (28)
Gx:CCR(U)
ET=CHARGING_CORRELATION_EXCHANGE (28),
Access-Network-Charging-Identifier-Gx:
Access-Network-Charging-Identifier-Value = 123,
Charging-Rule-Name = dynpcc1
Access-Network-Charging-Identifier-Gx:
Access-Network-Charging-Identifier-Value = 456,
Charging-Rule-Name = dynpcc2
Access-Network-Charging-Address
Gx:CCA
2. NPC sends this to IMS whether asked or not
Gx:CCR(U)
ET=CHARGING_CORRELATION_EXCHANGE (28),
Access-Network-Charging-Identifier-Gx:
Access-Network-Charging-Identifier-Value = 123,
IP-CAN-Session-Charging-Scope = 0,
Access-Network-Charging-Address
Rx: AAA
Access-Network-Charging-Identifier: Access-Network-Charging-Identifier-Value=123456
1. NPC would reject the AVP, now ok with 22.5
3. Ether message results in the same response
3’. NPC always reports this format to IMS

## Slide 162: 5G handling of Access-Network-Charging-Id
N7 Request
N7 Update – session level
N7 Update – per pcc rule
N7 Update – per flow
Aerospike commands
Commands
Confidential. Not for distribution or disclosure outside NOKIA
/usr/bin/curl -k -v -POST --http1.0 -H 'Content-Type: application/json' -d '{"supi": "imsi-310214000000051", "pduSessionId": "127", "pduSessionType": "IPV4", "dnn": "network1", "accessType": "3GPP_ACCESS", "ratType": "EUTRA", "servingNetwork" : {"mcc": 310, "mnc": 210}, "pei": "imei-8888888866666622", "ipDomain" : "Domain1", "ueTimeZone": "-08:00", "online": true, "offline": true, "3gppPsDataOffStatus": true, "ipv4Address": “11.1.3.50", "ipv6AddressPrefix": "1111:111:111:111:111:305:1002:8010", "notificationUri": "http://y.y.y.y:8082/npcf-smpolicycontrol/v1/sm-policies/n7-700001", "subsSessAmbr": {"uplink" : "100 Kbps", "downlink" : "100 Kbps"}, "refQosIndication": true, "subsDefQos": {"5qi": "9", "arp": {"priorityLevel": "9", "preemptCap": "NOT_PREEMPT", "preemptVuln": "NOT_PREEMPTABLE"}}, "suppFeat": "3D","sliceInfo":{"sst":1,"sd":"00009B"}, "accNetChId":{"accNetChaIdValue":1766051838,"sessionChScope":true}, "chargEntityAddr":{"anChargIpv4Addr":"172.17.104.241"}}' http://x.x.x.x:8080/npcf-smpolicycontrol/v1/sm-policies;
/usr/bin/curl -k -v -POST --http1.0 -H 'Content-Type: application/json' -d '{"repPolicyCtrlReqTriggers": ["AN_CH_COR"], "accNetChIds":[{"accNetChaIdValue":12345679,"sessionChScope":true}], "chargEntityAddr":{"anChargIpv4Addr":"172.17.104.241"}}' http://x.x.x.x:8080/npcf-smpolicycontrol/v1/sm-policies/N7-sps-ig-4-536f8e12-1757-4d90-ac45-3638ca6ab05b/update;
/usr/bin/curl -k -v -POST --http1.0 -H 'Content-Type: application/json' -d '{"repPolicyCtrlReqTriggers": ["AN_CH_COR"], "accNetChIds":[{"accNetChaIdValue":12345680,"refPccRuleIds":["MT:AUDIO MCN:1 FN:1 Rule#:1","MT:AUDIO MCN:1 FN:2 Rule#:2"]}], "chargEntityAddr":{"anChargIpv4Addr":"172.17.104.241"}}' http://x.x.x.x:8080/npcf-smpolicycontrol/v1/sm-policies/N7-sps-ig-4-536f8e12-1757-4d90-ac45-3638ca6ab05b/update;
/usr/bin/curl -k -v -POST --http1.0 -H 'Content-Type: application/json' -d '{"repPolicyCtrlReqTriggers": ["AN_CH_COR"], "accNetChIds":[{"accNetChaIdValue":12345680,"refPccRuleIds":["MT:AUDIO MCN:1 FN:1 Rule#:1"]},{"accNetChaIdValue":12345999,"refPccRuleIds":["MT:AUDIO MCN:1 FN:2 Rule#:2"]}], "chargEntityAddr":{"anChargIpv4Addr":"172.17.104.241"}}' http://x.x.x.x:8080/npcf-smpolicycontrol/v1/sm-policies/N7-sps-ig-4-536f8e12-1757-4d90-ac45-3638ca6ab05b/update;
aql -o json -c "select * from spspd1.SessionContainer"

## Slide 163: IPCAN session - before
Confidential. Not for distribution or disclosure outside NOKIA
Header about the Address but below is also the actual identifier
Sy session id reference appears in a “wrong place”
Completely out of place label for Location Info
Location Info under Maximum Bandwidth
Not sure what is this…

## Slide 164: IPCAN session - new
Confidential. Not for distribution or disclosure outside NOKIA
Removed header User Location
Label changed from AN Charging Address to Access Network Charging Information
Label changed from
AN Charging Id Value to
Access Network Charging identifier
The AVP name is not abbreviated, it is Access-Network; it is a grouped AVP indeed, no need to use the internal AVP with the “Value”
Removed Sy/Nchf Session Id from here, moved further down
Added the header and section here
Section moved furter down
Moved Logical and Physical Ids here, logically they belong here, they were added by 3GPP for Wireline
Moved Sy/NCHF here

## Slide 165
Agenda
Product overview & main benefits
Product functionalities
Interfaces & integration capabilities
Policy Rules
Main use cases

## Slide 166: Nokia Policy Controller
Key benefits
Comprehensive set of field-proven capabilities addresses wide range of use cases for 4G and 5G
Flexibility and simplicity in creating rules speeds up time to market
Production-level quality for 5G today!
Interoperability: Ease of network integration with built-in protocol manipulation
Leverages Nokia’s Common Software Foundation for speed, quality, and serviceability
Cloud-native with independently scalable sub-functions; stateless, microservices-based architecture with 99.999% application reliability
Always up-to-date: continuous delivery with in-service upgrades and automation via DevOps tools
Simplicity and ease-of-use based on common A.R.T. rule system with 150+ patents
Designed for fast multi-vendor deployments and fully pre-integrated with Nokia solutions such as Cloud Core

## Slide 167
Built for the demands of 5G and the scale of IoT
Nokia Policy Controller
Ultra high bandwidth / massive numbers of devices
  5G and IoT bring new demands on the core
Low latency / mobile edge computing
  Enable new use cases
Network slicing
  Increased flexibility for classes of devices
Could native architecture
  Provides scale, performance and flexibility

## Slide 168
Rule engine highlights
Nokia Policy Controller
The A.R.T. rules engine enables highly tailored, carrier-grade, policy control.
  New policy defined with in-product rules – not product change requests
  Empower innovation in marketing and services
  Roll out new policy easily, with rollback
  Compiled into a highly optimized form
  Tailored policy – without sacrificing performance and scalability
  4G and 5G policy in one place
  150+ patents

## Slide 169
Agenda
Product overview & main benefits
Product functionalities
Interfaces & integration capabilities
Policy Rules
Main use cases

## Slide 170
NPC Architecture
Layered Architecture View

## Slide 171: NPC Deployment Architecture
Mode of deployment – SM and ME

## Slide 172
NPC geo-redundancy
ME
OSS
NPC Site #1
NPC Site #2
Geo-replication
ME
Region 1
SM1
SM2
SM sites are Active-Standby (hot)
Service definition: SM has master copy & distributes to sites
SM selects device home or is instructed by OSS
SM maintains the device home location & each ME does geo-replication
Geo-replication
ME
NPC Site #3
NPC Site #4
ME
Region 2
Geo-replication
ME
NPC Site #5
NPC Site #6
ME
Region 3
Geo-replication
ME sites are Active-Active – No idle hardware
REST SOAP
1+1 mated pair
Multi-node support increases deployment flexibility for large operators by dividing into regions and supporting a combination of Policy and Charging nodes
Notes: reliability

## Slide 173: NPC SM & ME systems configured with all modules
Apps
ComSvcs
NPC SM System
Provisioning, API requests
OAME
API
IOH
Core
IOH
NPC ME System
DB
OAME
* Aux VMs host Service Discovery and Configuration (SDC) and always use exactly 5 VMs
5G, Diameter peers
Provisioning,
API requests,
SPR traffic
Notifications,
IT system interaction
DB replication
CDR
AUX*
SM App
IOH
DB
API to SPSs, IPv6 to ME
AUX*
Legend for VM engineering:
1 + 1
N + K
2*(N + K)
SU VM groups shown as gold, blue, and green boxes
DB replication
Operation and Management, logging
Operation and Management, logging
Provisioning, API requests, SPR traffic

## Slide 174: NPC VNF lifecycle management
Via Nokia CBAM VNFM
Create
Instantiate
Modify
Heal, auto-Heal
Backup, restore
Disaster recovery
Terminate
Delete
Scale out/in, auto-scale
Upgrade
  Life Cycle Events
  Instantiate VNF
  Healing
  Scale out /Scale –In
  Terminate VNF
  Delete VNF
  Backup and Restore
  VNF Network Upgrade
  VNF Disaster recovery
  Auto Healing
  Auto Scaling

## Slide 175
Agenda
Product overview & main benefits
Product functionalities
Interfaces & integration capabilities
Policy Rules
Main use cases

## Slide 176: Policy Management
NPC can provide the following to gateways (and TDFs)
  QoS, including rates (down/up) and priority
  PCC rules to define gateway behavior for a session/flow
  Redirects
  Charging related policies (such which rating group to use)
NPC can accept or reject/terminate sessions
It can register for events from the gateways (and TDFs)
  Be notified when events occur, such as a RAT Type change
  Receive a ‘call back’ from a gateway (Revalidation Timeout)
  Usage monitoring, such as reporting when a UE has used 20MB of data
Policies are provided on request and can be pushed for updates
Sample policy behaviors

## Slide 177: Policy Management
NPC provides the Policy Charging and Rules Function (PCRF) in 4G/LTE
  It provides policy to gateways (PCEFs) and other elements such as traffic detection elements (TDFs)
NPC provides the Policy Control Function (PCF) in 5G
  Both can be provided in the same NPC instance – a combined PCRF+PCF
NPC can provide tailored policy based on a wide variety of inputs, including
  Subscription type
  Type of device
  Location (such as MCC/MNC, GGSN IP address, cell tower)
  Configured subscriber/device data
  Time of day / day of week
  Usage related policies, such as CHF/OCS counter values
Policy control

## Slide 178: Policy Management
Networks need policy management
RNC
Gx
Sd
Sy
OCS
REST
Ud LDAP
Rx
NPC
AF/IMS
NPC can use NCC or a third-party OCS.
IMS
SGSN/SGw
GGSN/PGw
DPI
MME
OSS/BSS
SPR
Charging
PCRF
GERAN
CDN/ Video Opt.
Provides policy to network elements to enable subscriber experience

## Slide 179
Gx, Rx and Sy
NPC interfaces
Gx interface
Gateways (PCEFs) request policy for sessions
Policy can be highly customized using NPC rules
Changes in policy can be pushed to the gateways, such as due to a charging counter change or a provisioning change
Gateways notify NPC of network changes
Rx interface
Requests IMS bearers, eg voice (VoLTE) and video (ViLTE) and NPLI support
Typically works out-of-the-box with preset media type-QCI mappings
NPC adds Rx/Af support for independent voice/video allow/block which can be dependent on OCS counters
Sy interface
For use with NCC or 3rd party OCS
Policy can query the OCS counters and states
OCS notifies PCRF of changes in counters and states
NPC has support for multiple OCS, configured globally or per device

## Slide 180
Sd, LDAP/Ud and RADIUS
NPC interfaces
Sd Interface
Provides policy to traffic detection function (TDF) elements such as a DPI
Can be triggered on policy changes, in addition to policy provided over Gx
LDAP/Ud
Used for subscriber related lookups to an external SPR
Typically handed by a custom external SPR plugin which adapts the customer schema to the NPC schema

## Slide 181
Subscriber & External SPR/UDR
NPC interfaces
Internal SPR
Refers to users/devices being provisioned in NPC database
Device primary site can be optionally provided at provisioning. If not provided, NPC will select in round robin fashion
Primary site selection based on load and load rebalancing (roadmap)
External SPR/UDR
NPC retrieves data and caches it (audit for stale records supported)
Plug-in used by services to adapt the external schemas
Support for notifications to update cached fields
NPC adds support for SPR write-back
Nokia SPR/UDR
Leverage Nokia OneNDS and Nokia SDL (subscribers) as external SPR
Pre-integration with Nokia UDR
Roadmap

## Slide 182: Policy Management
Higher bandwidth, more devices, mobile edge computing, network slicing and more
Introduces policy management for access and mobility management
5G networks have a PCF in place of a PCRF
Data Network
NWDAF
NEF
BSF
AF
PCF
CHF
AMF
SMF
UPF
Nwdaf
Nnef
Nbsf
Naf
Npcf
Nchf
Namf
Nsmf
N4
RAN
N2
N3
N6
NRF
Nnrf
UDR
Nudr
Policy Control Function
Provides policy to network elements to enable subscriber experience
UDSF
Nudsf
NWDAF Network Data Analytics Function
NEF Network Exposure Function
NRF Network Repository Function
BSF Binding Session Function
AF Application Function
PCF Policy Control Function
CHF Charging Function
UDR Unified Data Repository
UDSF Unstructured Data Storage Func.
AMF Access & Mobility Mgmt Function
SMF Session Mgmt Function
UPF User Plane Function

## Slide 183: 5G and Policy
The following network functions (NFs) are key for policy in a 5G network
  PCF : the policy manager, 5G’s version of a PCRF
  SMF : the gateway, 5G’s equivalent of a PGW-C
    PGW-C indicates the control plane functions of a PGW
    PGW-U indicates the user plane functions of a PGW which are represented by the UPF in 5G
  AF/NEF : application function, similar to AF in 4G
  CHF : the charging function, similar to the OCS in 4G
    SPS also provides a CHF/OCS (SPS Charging)
  AMF : the access and mobility management function
    A new area of dynamic policy management
5G Key Policy Related NFs

## Slide 184: 5G Interfaces
The following network functions (NFs) are used by the PCF (and other NFs)
  NRF: allows NFs to discover each other, such as a PCF discovering a CHF
  UDR: subscription and policy data is stored in this common database
    Similar in function to external SPR but with a standardized schema
  BSF: provides a mechanism for an application to discover which PCF manages a session
    Nokia also provides a BSF NF
  UDSF: common database for session information
  NWDAF: network data analytics, such as providing network utilization information to NFs
5G key infrastructure NFs

## Slide 185: NPC
NPC will provide policy for both 4G/LTE (a PCRF) and 5G (a PCF)
Provides a single consistent view of a subscriber / device
Manage policies across both 4G and 5G
  Use common rules/information where appropriate, or 4G/5G specific rules when needed
Migrate subscribers more easily from the 4G network to the 5G network
Ease the migration to 5G
AF
PCF
CHF
SMF
AMF
Naf
Npcf
Nchf
Nsmf
Namf
PCRF
Gx
Rx
OCS
AF/IMS
Sy
RAN
UPF
SGSN/SGw
GGSN/PGw
4G
5G

## Slide 186: NPC Interfaces
Subscriber Profile Repository (SPR) / User Data Repository (UDR)
  System where subscriber data is maintained
Internal SPR
  NPC supports directly provisioned subscriber related data
  This is referred to as ‘internal SPR’
External SPR/UDR
  NPC supports querying an external SPR/UDR for subscriber related data
  This is referred to as ‘external SPR’ or ‘UDR’
Subscriber repository
Ud LDAP
NPC
UDR/SPR
PCRF+PCF

## Slide 187: NPC Interfaces
OSS / BSS systems
Service Manager
Similar API calls as DSC using the new subscriber model
External SPR notifications directed to Service Manager (SM)
Scalable
Highly scalable
Uses same architecture as NPC sites
3-tier stateless app design
Self-care highly scalable
Centralized
Common SM for all NPC sites
Provisioning systems don’t need to know which site a device is active on
NetAct connects to single SM

## Slide 188: NPC Interfaces
NPC can work with an external charging system
  N28 / Sy is used to communicate with a CHF/OCS (charging system)
NPC queries the CHF/OCS for counters and their state
The CHF/OCS notifies NPC of changes in counters and their state
  The policy rules may generate a policy push as a result
3rd Party charging systems
N28 / Sy
CHF/OCS
Charging
PCF+PCRF

## Slide 189
Agenda
Product overview & main benefits
Product functionalities
Policy Rules
Interfaces & integration capabilities
Main use cases

## Slide 190: Policy Management
Rules-based flexibility
  Each mapping can have multiple keys and outputs
  Used enter long list such as MCC/MNC location, cell tower lists, plans/OCS counter states, QoS related attributes, etc.
  Scripting editor rather than clicking forms
  Cut & paste rule code
  Autocomplete and syntax checking
  Decouple independent rule logic that can be called as variable in main Business Rules
  Can use Mappings for further simplification
New rules editor
Variables
Mappings
The core of the rules engine is carried forward from the DSC

## Slide 191
Policy rules: Why use a rules engine and what does it do?
OCS=Online charging system CHF=5G Charging function
Nokia Policy Controller
OCS/CHF
Network
Subscriber DB
Gateway/TDF
Other influencing events
Provides highly flexible and efficient policy definition
Rules are evaluated when an event occurs
Rules are only used when a custom policy is needed
When defining policy, or authoring rules, many inputs can be used to determine the policy
An easy and controlled way to move rules from the lab to production

## Slide 192: Dynamic policy control
Triggers
Flexible rules engine for high performance, highly customizable policy
Business rules set policy based on the operators needs
  Subscriptions, device type, location, access type, time based, customized … in combination
Subscribed plans
Type of device
Data available to rules
Business rules
Execute actions
Policy to gateway
Policy to TDF
Location
Access method
Day/Time
External
Internal
Message received
Cached sessions
Subscriber data
Custom data
Customized policy
Gx
N28
N7
Rx
Sy
Ud

## Slide 193: NPC Rules
Rules are edited in the GUI using a simple IF (condition) THEN (action) format
They are entered as text with autocompletion and syntax checking
Writing rules

## Slide 194: Sample use cases
Sample 1: Use case implemented using rules
Location based rules using MCC / MNC are common
  MCC is the country code
  MNC is the network code (within the country)
Example:
  MCCMNC 302100 is ‘home’
  Same country (MCC 302) is ‘regional’
  All others are ‘rest of world’
Location based: MCC / MNC roaming (rules only)

## Slide 195: NPC Rules
Tiered data rates / packages
Fair usage policy and actions
Policy based on OCS integration / counters
Policy based on specified AVP(s)
Zero-rated flows
Policy based on type of radio network (e.g., 3G, 4G, 5G, fixed)
Location based (roaming, in region, home)
Policy based on a lookup table (custom data)
Policy control based on device type (e.g., device model)
Bandwidth boost on demand
Policy control based on application, VoLTE, multi-screen video
Per-subscriber custom data for policy control
Secure network
Self-care / auto-registration
Notifications (redirection, SMS, email)
Enables a wide range of use cases
The A.R.T. rules engine is backed by more than 150 patents

## Slide 196
Agenda
Product overview & main benefits
Product functionalities
Policy Rules
Interfaces & integration capabilities
Main use cases

## Slide 197: Policy Management
To each their own…
Location based
(roaming, in region, home)
Device type based policy (type/model)
Use lookup tables (custom data)
Self-care and auto-registration
Time of day, day of week policies
Notifications (email, SMS, web service)

## Slide 198: NPC
A wide range of use cases and massive numbers of devices
Structural 5G deployment area
5G use case
In-vehicle infotainment
Truck platooning
Home
Hotspots
Healthcare
Drones
Highway use cases
Dedicated use cases
Dense city area use cases
Public transport use cases
8K video streaming
Hotspots
Events
Industry
VR/AR

## Slide 199: Sample use cases
Modern gaming relies more and more on access to servers
  Some services are beginning to stream games (servers do the heavy graphics work)
Gaming services require low latency …
Gaming experience
CPE
… not lag!

## Slide 200: Sample use cases
Gaming experience – standard connectivity establishment
Service based architecture
UPF
Home
AMF
SMF
FWA
PCF
NRF
UDM
2
1
3
NFP
1
UE triggers a PDU session establishment for the game
2
RAN sends PDU session establishment to AMF/5GC
3
PCF provides standard policy to AMF & SMF
4
SMF selects centralized UPF based on policy
4

## Slide 201: Sample use cases
Gaming experience – standard connectivity
Service based architecture
UPF
Home
AMF
SMF
FWA
PCF
NRF
UDM
NFP
The user is now playing
… with the traffic going to the centralized UPF
… resulting in lag and a poor experience

## Slide 202: Sample use cases
Gaming experience – premium connectivity establishment
Service based architecture
UPF
Home
AMF
SMF
FWA
PCF
NRF
UDM
2
1
3
NFP
1
UE triggers a PDU session establishment for the game
2
RAN sends PDU session establishment to AMF/5GC
3
PCF provides premium policy to AMF & SMF for use of LADN including premium QoS
4
SMF selects LADN UPF and uses premium QoS
4
Use of a Local Area Data Network (LADN) for the gaming servers for a given area can greatly reduce lag for the service
UPF

## Slide 203: Sample use cases
Gaming experience – premium connectivity
Service based architecture
UPF
Home
AMF
SMF
FWA
PCF
NRF
UDM
NFP
The user is now playing
… with the traffic going to nearby UPF with premium QoS
… resulting in a great gaming experience
UPF

## Slide 204: Sample use cases
Custom data can be added to devices
  Operator-defined fields
  Provisioned with the device
    Or retrieved from an external database for the subscriber/device
NPC rules can use custom data in conditions
  Can have policy dependent on one or more operator-defined fields
  Can use custom data in combination with other fields
Example shows a “ServiceTier” with value “bronze”
Subscription based policy

## Slide 205: Sample use cases
A variety of location information is available to determine policy
MCC / MNC indicates which network a device is on
  Can be used for roaming scenarios
Cell tower Ids can be used for fine-tuned location information
  Such as policy at a subscribers home location
  Or in/around metro/subway stations
The gateway IP address can be used
  Sometimes used if MCC / MNC are not sufficient
Location based

## Slide 206: Sample use cases
Sample 1: Use case implemented using rules
Location based rules using MCC / MNC are common
  MCC is the country code
  MNC is the network code (within the country)
Example:
  MCCMNC 302100 is ‘home’
  Same country (MCC 302) is ‘regional’
  All others are ‘rest of world’
Location based: MCC / MNC roaming (rules only)

## Slide 207: Sample use cases
Sample 2a: Implemented using a variable
  Define a “Region” variable
  Type ‘string’
Region has one of these values
  “Home”, “Regional” or “World”
Assigned based on MCCMNC
Location based: MCC / MNC roaming (variable and rules)

## Slide 208: Sample use cases
Sample 2b: Using the “Region” variable
These rules are simpler to write and read
Only one place to change to update region details
  If more MCCMNCs are included in a region, for example
Location based: MCC / MNC roaming (variable and rules)

## Slide 209: Sample use cases
Works out-of-the-box
Default mapping from Rx to Gx AVPs / N7 fields provided
  Such as Media-Type AUDIO to Gx QCI 1
  Easy to override in rules
VoLTE

## Slide 210: Sample use cases
The names and values of CHF/OCS counters can drive policies
In this example the speed is determined based on a counter called “counter1”, where
  Status “th3” gives 50000/50000
  Status “th4” gives 35000/35000
CHF/OCS counters

## Slide 211: Sample use cases
Per subscriber/device set time spans
  Can be within a day, or across days
Each interval has a ‘Tag’
  Can have sets of intervals for different uses
Time of day / day of week configuration

## Slide 212: Sample use cases
Rules provide the appropriate policy
Time of day is flexible
  Allow/disallow access
  Set QoS changes
  Apply different PCC rules
For shown:
  During any “app1” interval set PCC rule “app1_on”
  Otherwise set PCC rule “app1_off”
Time of day / day of week rules

## Slide 213: Sample use cases
NPC provides the usage control service
Similar to that provided by the DSC
UCS is available at the session level
Gx metering

## Slide 214: Sample use cases
Similar to the examples shown, rules can be tailored in many ways, including
  Policy based on the DNN/APN – different privileges for different DNNs/APNs
  Policy based on the slice (5G)
  User equipment type based policy
  Access type dependent policy (such as by RAT-Type)
Policy may push PCC rules to the gateway
  Can enable redirects of flow-based handling of traffic
The policy rules can send notifications to the subscriber
  By email, SMS or web service call
OSS/BSS facing APIs allow for self-care
  Subscribers can be provided a portal to configure policies
Many possibilities…

## Slide 215: Alarms Architecture
CSF Harmonized (Unified logging) API
It’s in JSON format (set of key-value pair) with predefined keys
Supported backend is ETCD
Management via “calm-alma” service on Active OAME node
“calm-alma” service is dependent on “rsyslog” service
Service will be UP on Active OAME
By default at any time 1K (in count) active alarms can be stored in backend
File structure
      /etc/alma: directory for alarm service configuration
      /var/log/calm/alma.log: All the SNMP traps are captured in this this file
      /var/log/calm/history.log: All the cleared alarms are moved into this file
      /var/log/calm/alarms.log: If backend limit is reached, alarms will be dumped into this file
List all the active alarms (On Active OAME node only)
curl http://localhost:8182/api/alma/alarms -v | python -m json.tool

## Slide 216: Flow of Alarms
App node to OAME node

## Slide 217: Flow of Alarms
App node to OAME node

## Slide 218: Sample SPS Alarms
Alarm generate at App node
Alarm sent to OAME node
Cleared alarm

## Slide 219: Notification Service
Notification Service (NS) notifies subscribers about charging and policy events, like using up a data bundle, or being slowed down to 3G speeds through communication methods chosen by the subscriber. NS is present in every SPS deployment.
The notification service can be used to send notifications to the subscribers, or external back office systems. For example, an operator might want to alert the subscribers of an upcoming festival offer. These notifications can be sent over SMS or email, depending on the subscriber's preference. Other preferences can also be set such as to receive notifications only in a specified time of day, for example, from 6 PM to 10 PM only. The subscribers can also opt out of the notification service.

## Slide 220: Distributed System - Provisioning (HTTP) Call Flow
SM GUI (Charging, NS, Policy)
ME-IOHO
ComSVC0
ComSVC1
SOAP
SOAP Provisioning
SOAP Provisioning
SM-IOHO
SM0
SM1
REST
SM CLUSTER
ME CLUSTER

## Slide 221
Distributed System - E2E Call Flow
ME-IOHD
Charging Node
ME-IOHO
ComSVC0
ComSVC1
SPS NS Container
SPS NS Container
REST
Call Execution
Call Execution
Notification Client
TCP
EMAIL
TCP
EMAIL

## Slide 222: NS – E2E Email Call Prerequisites
Create Email Server Entity
Create Notification Profile
Create Notification Template
Create Device
Create User

## Slide 223
Create Email Server

## Slide 224
Create Notification Profile

## Slide 225: Create Notification Template

## Slide 226: Create Device

## Slide 227
Create User